## Slide 1
Architectures for Secure Quantum Computing Systems
Prof. Jakub Szefer
Computer Architecture and Security Lab – CASLAB
Dept. of Electrical Engineering
and Dept. of Computer Science (by courtesy)
Yale University
https://caslab.io/jakub

## Slide 2: Quantum Computing Today
… 2025
4159 qubits
IBM projection
2025
$
… 2022
433 qubits
IBM
Nov. 2022
… 2033
May 2023 announcement of 100,000 qubit computer for 2033
The field of quantum computing is undergoing rapid development
  Quantum computers are in infancy, but holds potential in that they could solve complex problems
  Promise advances in life-saving drugs, green-battery technology, etc.
  They will process or store valuable intellectual property
Quantum computers are already cloud-based
  Remote users can access them easily
  But open to attack by malicious users
  Further threats of untrusted cloud providers
Need to analyze and secure quantum computer architectures today
Cloud
Providers
IBM Quantum
Microsoft Azure
Amazon Braket

## Slide 3: Architectures for Secure Quantum Computing Systems

## Slide 4: Typical Quantum Computer System Overview
Analog RF Pulses
Digital Signals
Cloud-based Access
Management Server
Quantum Computer Controllers
Network Packets
Quantum
Processing
Unit
Quantum Program
Quantum Program Compiler
Classical Co-processor
Network Packets
Digital Signals
User

## Slide 5: Typical Quantum Computer System Overview
Abstract view of the quantum computer system can aid in analyzing the potential security threats:
User
Cloud
Digital
Signals
Digital
Signals
Analog
Signals
CPU
DAC / ADC
CPU
Digital
Signals
Solution: classical encryption methods
Solution: classical encryption methods
What are threats and possible protections at each ?

## Slide 6: Assumptions and Threats
Assume honest-but-curious attackers
  Do not inject errors or manipulate signals
  Only eavesdrop on operation of the quantum computer and any signals
Resulting attack surface:
  Cloud (CPU)
  Controller (CPU)
  Controller (DAC)
  QPU
User
Cloud
Analog
Signals
CPU
DAC / ADC
CPU
Digital
Signals

## Slide 7: QC-TEE: An Architecture for Trusted QPU

## Slide 8: Quantum Computer Trusted Execution Environment
Demonstrate how introduction of trusted components in the QPU can help protect from malicious cloud providers
Inspired by trusted hardware in classical computers
  Trade improved security for extra hardware and trust in manufacturer
Added features in the QPU can help hide circuits executing on the QPU
  No need for blind quantum computation
  Simple logic to be added into QPU
Theodoros Trochatos, Chuanqi Xu, Sanjay Deshpande, Yao Lu, Yongshan Ding, and Jakub Szefer, “A Quantum Computer Trusted Execution Environment,” Computer Architecture Letters (CAL), 2023. Best of CAL Selection (to be presented at HPCA 2024).
User
Cloud
Digital
Signals
Digital
Signals
Analog
Signals
CPU
DAC / ADC
CPU
Digital
Signals

## Slide 9: Remote Execution of Quantum Circuits
Analog RF Pulses
Digital
Signals
Cloud-based Access
Management Server
Quantum Computer Controllers
Network Packets
Quantum
Processing
Unit
Quantum Program
Quantum Program Compiler
Classical Co-processor
Network Packets
Digital Signals
User
Users submit circuits that are processed by the cloud provider, and eventually issued to quantum computer controller for execution on the quantum computer

## Slide 10: QC-TEE Assumptions
Focus on superconducting qubit quantum computers
Fridge of superconducting qubit quantum computers can form natural trust boundary
  Temperature and pressure changes can be easily detected when fridge is opened
Key idea: need to protect or obfuscate the analog RF pulses going into the (trusted) QPU

## Slide 11: High-Level Idea of Hiding Control Pulses
Analog control pulses cannot be ”encrypted” unlike digital information, but we can hide or obfuscate them instead
  Input user circuit:
  Circuit with decoy pulses:
  Decoy pulses attenuated in the QPU
q1
q2
q0
q3
q1
q2
q0
q3
q1
q2
q0
q3

## Slide 12: Trusted Hardware for Attenuation of Control Pulses
Decryption Engine
TRNG
Attenuation Switches
Switch Control Module
To Qubits
Encryption
Engine
Encrypted output bitmap sent to user
Input RF Pulses
Encrypted Input Bitmap
Digital signals
RF pulses
Input Bitmap Mem.
QC-TEE
Load Bitmap
Trigger Start
q1
q2
q0
q3
q0: 0 1 0 0 0 0 0 0
q1: 1 1 1 1 0 0 0 0
q2: 0 1 1 0 1 1 1 1
q3: 0 0 1 0 1 1 1 1
q1
q2
q0
q3

## Slide 13: End-to-End Operation
Software needs to generate the decoy pulses and the bitmap, while hardware attenuates the pulses in side the fridge:
H
X
Modified Compiler
(e.g. part of Qiskit)
Input User
Quantum Circuit
Remote User
Quantum Computer Provider
Quantum
Computer Manager
Runtime
(e.g. part of Qiskit)
Generate Control Pulses for User’s Circuit
Mix Control Pulses with Decoy Pulses
Generate Input Bitmap
Encrypt Input Bitmap using AES-GCM and shared secret key which is generated using PQC-KEM and Public Key of the Backend
Send Transpiled Circuit including Mixed Decoy Pulses
Send Encrypted, Signed Input Bitmap
Decrypt Input Bitmap using AES-GCM and shared secret key generated in step 4
De-Mix Decoy Pulses
Execute Circuit

## Slide 14: Evaluation Setup
We evaluated different configurations:
  Baseline
  One-sixteenth-delay
  Quarter-delay
  Max-delay
Further for all the levels, except baseline, we analyze results with and without a randomize-output option
Evaluated on:
  7-qubit IBM Perth, to test small-scale benchmarks
  27-qubit IBM Algiers, through the Pay-As-You-Go plan on IBM Cloud to test medium-scale benchmarks
  Aer simulator
q1
q2
q0
q3
q1
q2
q0
q3
Quarter-delay vs. Max-delay example

## Slide 15: Evaluation Using Variational Distance
Worst case Variational Distance (VD) for the QASM-Bench benchmarks considering perfect RF switches and emulating imperfect RF switches (99.99% amplitude attenuation)
Worst case Variational Distance (VD) for the QASM-Bench benchmarks for machines with different Quantum Volume (QV)

## Slide 16: Evaluation of Benchmark Correctness
Evaluation of correctness of 22 QASM-Bench benchmarks assuming imperfect RF switches (99.99% amplitude attenuation), all benchmarks show correct results

## Slide 17: Security Analysis
The cloud provider is able to see all the (real and decoy) control pulses, but needs to figure out which ones are real and which are decoy
The complexity based on our analysis:
Number of possibilities is much beyond 2256 combinations that cloud provider would have have to consider

## Slide 18: Open Challenges in Securing Quantum Computer Architectures
User
Cloud
Digital
Signals
Digital
Signals
Analog
Signals
CPU
DAC / ADC
CPU
Digital
Signals
Cloud (CPU) | Controller (CPU) | Controller (DAC) | QPU
Untrusted | Untrusted | Untrusted | Untrusted
Untrusted | Untrusted | Untrusted | Trusted
Untrusted | Untrusted | Trusted | Untrusted
Untrusted | Untrusted | Trusted | Trusted
Untrusted | Trusted | Untrusted | Untrusted
Untrusted | Trusted | Untrusted | Trusted
Untrusted | Trusted | Trusted | Untrusted
Untrusted | Trusted | Trusted | Trusted
Cloud (CPU) | Controller (CPU) | Controller (DAC) | QPU
Trusted | Untrusted | Untrusted | Untrusted
Trusted | Untrusted | Untrusted | Trusted
Trusted | Untrusted | Trusted | Untrusted
Trusted | Untrusted | Trusted | Trusted
Trusted | Trusted | Untrusted | Untrusted
Trusted | Trusted | Untrusted | Trusted
Trusted | Trusted | Trusted | Untrusted
Trusted | Trusted | Trusted | Trusted
Developed first architecture for securing quantum computation in the cloud
Still, many unexplored configurations still need to be studied
Analyze tradeoffs between cost and security protections
Develop different threat models and use-cases

## Slide 19
Thank You!
https://caslab.io/jakub
Prof. Jakub
Szefer
Chuanqi
Xu
Theodoros
Trochatos
Sanjay
Deshpande